## Slide 1: TCP/IP Programming
presented by
Mujtaba Khambatti
Portions of slide content from Opus1 (© 1996), TGV Software, Inc. (© 1996), Process Software Corp. (© 1996), Hari Balakrishnan (© 1998-2002), Addison-Wesley Publishers Limited (© 1990, 1994), Pearson Education Limited (© 2001)
CSE 531

## Slide 2: Contents
Terms and Concepts
Sample Routines and Libraries
Advanced Topics

## Slide 3: Terms and Concepts
TCP/IP Programming

## Slide 4: The Famous OSI model
Application
Presentation
Session
Transport
Network
Data Link
Physical
Network
Data Link
Physical
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 5: Usually TCP/IP has 4 layers
Application (HTTP/SMTP/...)
Transport (TCP/UDP)
Network (IP)
Data Link & Physical
Network (IP)
Data Link & Physical
Application (HTTP/SMTP/...)
Transport (TCP/UDP)
Network (IP)
Data Link & Physical

## Slide 6: TCP Overview
Transmission Control Protocol
First defined in RFC-793
Connection-oriented protocol
End-to-end stream of data

## Slide 7: UDP
User Datagram Protocol
First defined in RFC-768
Connectionless protocol
Unreliable datagram delivery

## Slide 8: What is Client-Server?
TCP/IP networks are client-server
Application-to-Application
Inter-Process Communication (IPC) used between Client and Server processes
Popular TCP/IP based IPC:
  Sockets (Berkeley UNIX)
  TLI (AT&T UNIX System V)

## Slide 9: Sockets
OS independent, standardized API
Communication end-point
Makes the network look like a file system
File System | Sockets
OPEN file | OPEN connection
CLOSE file | CLOSE connection
READ | RECEIVE / READ
WRITE | SEND / WRITE

## Slide 10: Network interface looks like a file
Application Process
write()
read()
read()
write()
Application Process

## Slide 11: Network Byte Order
High order byte
Low order byte
Low order byte
High order byte
Address n
Address n+1
Address n
Address n+1
Little endian
Big endian
convert
Motorola 68xxx
IBM 370
Intel 80x86
VAX & Alpha (VMS)

## Slide 12: Encapsulation of message
Application Data
TCP header
IP header
Ethernet header
Ethernet frame
Trailer
HTTP header

## Slide 13: Segmentation and Reassembly
TCP
IP
“I am a message”
“I am a
message”
“I a
m a
mess
age”
TCP
IP
“I am a message”
message”
“I am a
age”
m a
“I a
mess
Application
Data Message
TCP Segments
IP Packets

## Slide 14: Addressing entities in a network
TCP/IP layers have 2 part addresses:
  Address of everything below it + Address of itself
Sometimes lower-level addresses are implied.
  e.g. Ethernet MAC  IP address
3 addresses are important
  Application level address (Servers in RFC 1700, <1024)
    16 bit integers, SMTP port=25
  Transport level address (assigner IANA, RFC 1700)
    8 bit protocol numbers, TCP=6, UDP=17
  Network level address (assigner InterNIC, manager admin)
    32 bit integers, 249.229.24.15

## Slide 15: Network Addresses
Triplet (IP, Protocol, Port) identifies a process
2 Triplets identifies a connection
  Also called a socket / socket pair
Application number (port) 3333
On protocol number 6 (TCP)
At IP address 249.229.24.18
Application number (port) 25
On protocol number 6 (TCP)
At IP address 192.246.25.7

## Slide 16: Incoming Connections: Servers
Your Application
Network Kernel
If anything should come in for Port 25 on TCP, give it to me. I will be waiting right here.
OK
Daemon Approach
Your Application
Network Kernel
Port 25? I will start a new process running Your Application and hand it this call.
Here is an incoming call.
InetD Approach
InetD

## Slide 17: Sample Routines and Libraries
TCP/IP Programming

## Slide 18: TCP/IP Programming Models
Berkeley Sockets popularized in 1986
  Wide implementation (Windows, UNIX, VMS,…)
Other models
  STREAMS model (UNIX System V)
  …

## Slide 19: Socket
Communications end-point
Data structure within the kernel
Protocol Family
Service
Local Address
Remote Address
socket
AF_UNIX: UNIX domain sockets
AF_INET: Internet Protocols
AF_NS: Xerox NS Protocols
SOCK_STREAM: TCP stream socket
SOCK_DGRAM: UDP Datagram socket
SOCK_RAW: Raw IP socket
integer
integer
sockaddr: a 2-octet address family identifier and then 14-octets of address specific information
struct sockaddr_in {
u_short sin_family; /* AF_INET */
u_short sin_port; /* 16 bit port # */
struct in_addr sin_addr; /* 32 bit IP addr */
char sin_zero[8];
}

## Slide 20: Socket: Connection-oriented
socket()
bind()
listen()
accept()
read()
write()
close()
socket()
connect()
write()
read()
close()
Block until connection from client
Server
Client
}
Replaces file open()
{

## Slide 21: Socket: Connectionless
Client-Server is simpler
socket()
bind()
recvfrom()
sendto()
socket()
bind()
sendto()
recvfrom()
Block until data from client
Server
Client

## Slide 22: Client: socket()
int socket(int domain, int type, int protocol)
int s, domain, type, protocol;
domain = AF_INET; /* always the same */
type = SOCK_STREAM; /* TCP */
protocol = 0;
s = socket(domain, type, protocol);
if (s < 0) ERROR(“Cannot create socket!”);

## Slide 23: Client: connect()
#define SMTP_PORT 25
#define IP_ADDRESS 0xF9E50F12 /* 249.229.15.18 */
struct sockaddr_in sin;
int connect(int s, struct sockaddr* name, int namelen);
int status;
sin.sin_family = AF_INET;
sin.sin_port = htons(SMTP_PORT);
sin.sin_addr = htonl(IP_ADDRESS);
status = connect(s, (struct sockaddr*)sin, sizeof(sin));
if (status != 0) ERROR(“Cannot connect to other side!”);

## Slide 24: Client: read() / write()
char buf[LINELEN+1];
while ( (n = read(s, buf, LINELEN) ) > 0) {
fwrite(buf, n, 1, stdout);
if (!fgets(buf, LINELEN, stdin)) break;
write(s, buf, strlen(buf));
}
if (n < 0) ERROR(“Cannot read from socket!”);

## Slide 25: Client: close()
status = close();
if (status != 0) ERROR(“Cannot close socket!”);

## Slide 26: Server: socket()
int socket(int domain, int type, int protocol)
int s, domain, type, protocol;
domain = AF_INET; /* always the same */
type = SOCK_STREAM; /* TCP */
protocol = 0;
s = socket(domain, type, protocol);
if (s < 0) ERROR(“Cannot create socket!”);

## Slide 27: Server: Local addresses
#define SMTP_PORT 25
#define IP_ADDRESS 0xF9E50F12 /* 249.229.15.18 */
struct sockaddr_in sin;
sin.sin_family = AF_INET;
sin.sin_port = htons(SMTP_PORT);
sin.sin_addr = INADDR_ANY; /* Don’t care about addr */

## Slide 28: Server: bind() & listen()
#define MAX_BACKLOG 5
int bind(int s, struct sockaddr* name, int namelen);
int listen(int s, int backlog);
int status;
status = bind(s, (struct sockaddr*)sin, sizeof(sin));
if (status != 0)
ERROR(“Cannot bind to local address!”);
status = listen(s, MAX_BACKLOG);
if (status != 0)
ERROR(“Cannot ask kernel to listen!”);

## Slide 29: Server: Blocking accept()
int accept(int s, struct sockaddr* addr, int* addrlen);
int status, addrlen, vs;
struct sockaddr_in sin2;
addrlen = sizeof(sin2);
vs = accept(s, (struct sockaddr*)&sin2, &addrlen);
if (vs < 0) ERROR(“Cannot accept connection!”);

## Slide 30: Server: read() / write()
/* Get line from client */
read(vs, buf, 256);
/* Write to client */
write(vs, buf, strlen(buf));

## Slide 31: Server: close()
status = close();
if (status != 0) ERROR(“Cannot close socket!”);
Try doing UDP on your own!

## Slide 32: Byte Order
Always use byte order routines to:
  Look inside protocol headers
  Call protocol routines
u_long htonl(u_long hostlong);
u_short htons(u_short hostshort);
u_long ntohl(u_long netlong);
u_short ntohs(u_short netshort);

## Slide 33: Inet & netdb routines
Internet address conversions
  char* “249.229.15.18” to 0xF9E50F12
u_long inet_addr(char *cp);
char* inet_ntoa(struct in_addr in);
What about converting “www.asu.edu”
  Use DNS (gethostbyname(),gethostbyaddr())

## Slide 34: Advanced Topics
TCP/IP Programming

## Slide 35: Gateways
Facilitate communication between different networks in an internetwork
Two approaches:
  Translation based
    Translate headers and protocols
    OSI X.25/X.75
  Unified Network Layer

## Slide 36: Standards Process
Involves people from different organizations
IETF (Internet Engineering Task Force)
  Meets every 4 months
  Short-lived groups (usually <2 years)
  “Rough consensus” (no voting)
  Publishes RFC (Request For Comments)
  Internet Drafts precede an RFC

## Slide 37: IPv4 Addressing
IPv4 (1981 RFC-791) had 32 bit addresses
Addresses divided into classes
  Class A: start with 0, next 7 bits- network id, last 24 bits-hostid
  Class B: start with 10, next 14 bits-network id, 16 bits – host id
  Class C: start with 110, next 21 bits-network id, 8 bits – host id
  Class D: start with 1110, next 28 bits for group address
  Addresses starting with 1111 are reserved for experiments
1984 – Subnet masks introduced
1990s – IETF deployed CIDR (Classless Inter-Domain Routing) because the 214 Class B addresses were running out.

## Slide 38: IP Fragmentation & Reassembly
Different networks have different MTU (Maximum Transmission Unit)
Gateway
Network 1
Network 2
If IP header flag = DO NOT FRAGMENT
then discard packet
Else
fragment packet into MTU-sized fragments

## Slide 39: Flow Control
Modern TCP receivers implement a delayed ACK (receiver to sender)
  ACK alternate packets iff in-sequence arrival
  Must ACK at least once every 500ms
ACK contains window size
  Space available in receivers socket buffer
Different from congestion control!
Sender will wait for ACKs. Uses timeout
Timeout value calculated as a running average of RTT (Round Trip Time)

## Slide 40: Networking Tools
tcpdump
  Places device driver into promiscuous mode
  Receive all transmitted and received packets
  Filter ones of user’s interest  user process
dig / nslookup / whois
  DNS lookup tools
  Query Address registries
ping / traceroute
  ICMP “Echo Request” waits for “Echo Reply”
  Get an idea about route from a host to a destination

## Slide 41: More information
Donald A. Curry, “Using C on the UNIX System”, O’Reilly and Associates.
Douglas Comer, “Internetworking with TCP/IP Volume III”, Prentice-Hall.